## Slide 1: Self Tuning Adaptive Regulation of a PI(D) Controller

## Slide 2: Abstract
Novel Self tuning adaptive algorithm for automatic tuning of PI(D) controllers.
Aims at resolving the drawbacks of present tuning techniques.
Also supports online tuning i.e. we can change the controller parameters during the time of tuning.
The objective is to attain a design-point on the Nyquist diagram.
By injecting sinewaves and employing a PFE, closed-loop adaptive tuning is possible and there is exact convergence to the design-point without the approximations of describing-function theory

## Slide 3: Shortcomings of Previous Methods:
Relay Autotuning:
    Offline tuning method, no control can be provided during tuning
    Load disturbances also influence the estimation accuracy
    Use of describing function analysis leads to incorrect estimate of frequency point
Open Loop Tuning:
    Sensitivity to disturbances
    Use of parametrised process model leads to lack of generality.
    Only suitable for Offline tuning

## Slide 4: Expectations from Controller
The controller proposed is supposed to have positive points of relay based tuning which include its ease of use and speed.
It is also expected to have greater flexibility, giving superior PID tuning.
It must also have Robustness to:
  noise,
  set-point changes
  disturbances .

## Slide 5: What is Adaptive Algorithm?
Aims at finding out best adjustment of controller parameters in face of changing process dynamics
Measures the performance relative to a given Index of Performance and modifies it to reach to a optimum value
Major 3 components:
  Identification
  Decision
  Modification

## Slide 6: Algorithm
Self tuning Regulator
Benefits:
  Flexible
  Easy to understand
  Easy to implement with muP

## Slide 7: Algorithm
Composed of 2 loops
Inner loop
  Process
  Ordinary feedback controller
Outer Loop
  Used to adjust the parameters of the feedback controller
  Composed of
    recursive parameter estimation
    adjustment mechanism for controller parameter
The parameters in process are updated via online training

## Slide 8: Adaptive Control: Identification
A process by which the system is characterised or by which the IP(Index of Performance) value is measured.
Here : gain estimators

## Slide 9: Adaptive Control : Decision
Here, the IP measurements are analysed to decide how system performance relates to the desired optimum
If performance is inadequate
  Corrective adjustments are made according to the established stratergy
Here : Design Block

## Slide 10: Adaptive Control : Modification
Process of changing system parameters towards the optimum setting based on the instructions received from identification and decision processes
Here : PFE(Phase/Frequency Estimator)

## Slide 11: System Block Diagram
Important Blocks:
PFE Block(Phase Frequency Estimator)
GE Block (Gain Estimator)
Design Block
Controller Block
Plant Transfer Function Block

## Slide 12: PFE
Injects a variable frequency sine wave to our system
It then changes the frequency until the desired phase margin is reached

## Slide 13: Simulation Block For PFE

## Slide 14: Controller
Assumption: We have implemented the PI controller tuning
Parameters:
      Ti : output from the Design Block
      from the Design Block

## Slide 15: Controller

## Slide 16: VBPF(Variable Band Pass Filter)
Utility:
  elimination of DC values;
  attenuation of harmonics, arising for example if there are nonlinearities in the plant or actuator;
  reduction in the effect of additive noise.

## Slide 17: Simulation Block : VBPF

## Slide 18: Amplitude Estimator Design

## Slide 19: GE
Estimates the Plant Gain and thus give the output to the design block

## Slide 20: Design Block
It takes the input from GE , and calculates the Ti, and Kp using the design rules specified in the paper
K Calculation; 2K’
Calculation of K’ and Ti

## Slide 21: Design Block
Calculation of Ti

## Slide 22: Plant
2 types of plant
    Type 0 : No poles at origin
    Type 1 : 1 pole at origin
3rd order and 7th order transfer functions taken
It receives the control signal from the controller and produces the plant output
This plant output and controller output is given to a GE and thus we get an estimate of the Gain

## Slide 23: Adaptive Gain
This is the factor that affects how big are the steps taken by the PFE
while changing the frequency
We have directly chosen the value, (There were separate papers being written regarding the selection of Adaptive Gain)
Due to the time varying effect of the controller parameters , we scaled the adaptive gain appropriately.
For type 0 plant : 4- rescaling factor
For type 1 plant : 8 – rescaling factor

## Slide 24: PSD
The input nodes correspond to signals from the VBPF (the
plant's response, being the upper input to the algorithm) and the present frequency and (the PLL’s current phase), whilst the output is the
(possibly filtered) error signal S,(t) that drives the updating
integrator.

## Slide 25: Design Point: D1
                Whole algorithm depends on selection of design point D1.
                Once design point D1 is selected
                the corresponding desired phase margin is used to calculate the desired phase shift .
                Initially, the frequency which is fed to PFE is very close to the frequency at the desired phase margin(design point)

## Slide 26: Initialisation

## Slide 27: Initialisation
The adaptation of the test frequency (w1) and the plant gain estimate Gp(jw1) is halted for a period = 2(Td + ).
    To allow the responses of the estimators to settle before they embark on adjusting the controller parameters,
Where relates to the dead-time in the PFE and GE resulting from the use of Hilbert transformers

## Slide 28: Various Formulaes/Assumptions:
Selection of parameter ‘a’:
      Lambda : Td/T
      Td : deadtime got from FODT model
      PM : desired phase margin

## Slide 29: Response Based Selection
Phase Margin : 60
Graph plotted for step response for different values of a

## Slide 30: Simulation Results by Author
Simulation result for 7th order system – Type 0 plant
Simulation result for 3rd order system – Type 1 plant

## Slide 31: Simulation Comparisons by Author
Simulation for FODT with = 2 0.5

## Slide 32: A Special Thanks….
Dr. Guillermo Valencia Palomo
Link to Profile

## Slide 33
-Group 17
Ayush Agrawal(2018A8PS0469P
Pranamya Jain(2018A8PS0769P)
Nitin Pant (2018A8PS0381P)
THANK YOU